## Slide 1: q-PCR Real Time Quantitative Polymerase Chain Reaction
Melissa Nicole Moyer

## Slide 2: q-PCR
Information
Methods
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
  Background
  Results
  Conclusion

## Slide 3: Information
Real Time Quantitative Polymerase Chain Reaction (q-PCR)
  Works like regular PCR where you amplify a desired gene
  Differences from regular PCR:
    Quantifies (counts) the amount of PCR Product
    You can watch the products being produced in real time!
A Rotor-Gene Q can be used to preform q-PCR
  Methods will be explained based off of the Rotor-Gene Q and its 72-Well Rotor for up to 72 0.1 ml strip tubes with caps

## Slide 4: q-PCR
Information
Methods
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
  Background
  Results
  Conclusion

## Slide 5: Methods
Ingredients:
Purified DNA
taq Polymerase
Nucleotides
Primers
MgCl2
Buffer
Nuclease-free water
Double stranded DNA Dye – such as SYBR Green
Kits can be ordered with most of the ingredients mixed together. The primers, nuclease-free water and the purified DNA are the missing components.

## Slide 6
10-50 µL total volume per tube is recommended for the above four strip tubes.
The tubes are then placed in the Rotor which is placed in the Rotor-Gene Q
There are several other tubes that can be used with this machine for q-PCR
Methods
http://www.qiagen.com/media/product-tools/flash/RotorGeneQ/360/index.html

## Slide 7
95 ºC for3 minutes
35 cycles of:
  94 ºC for 45 seconds
  60 ºC for 45 seconds
  68 ºC for 120 seconds
Methods
http://www.qiagen.com/media/product-tools/flash/RotorGeneQ/360/index.html

## Slide 8
A light passes through the samples and is read by the sensors as the reactions are denaturing, annealing, amplifying and spinning around
Methods
http://www.qiagen.com/media/product-tools/flash/RotorGeneQ/360/index.html

## Slide 9
Methods

## Slide 10: q-PCR
Information
Methods
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
  Background
  Results
  Conclusion

## Slide 11: Background
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
Julio Go´mez-Rodrı´guez, Valance Washington, Jun Cheng, Amalia Dutra, Evgenia Pak, Pentao Liu, Daniel W. McVicar and Pamela L. Schwartzberg
Received March 31, 2008; Revised July 28, 2008; Accepted July 31, 2008; Published online 18 August 2008
Nucleic Acids Research, 2008, Vol. 36, No. 18 e117

## Slide 12: Background
The authors studied:
The accuracy of q-PCR by comparison to Southern Analysis
The accuracy of fluorescent in situ hybridization (FISH) compared to q-PCR

## Slide 13: q-PCR
Information
Methods
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
  Background
  Results
  Conclusion

## Slide 14: Results
Figure 1

## Slide 15: Results
Figure 2

## Slide 16: Results
FISH
  36% targeting frequency when there was only a 14% Tec construct.
  There were weakened signals suggesting partial BAC integration into the genome.
    This lead to weakened signals at the places of random short insertions.
q-PCR revealed:
  The multiple inserts of BAC into the Genome
  There are both false positives AND false negatives with FISH

## Slide 17: q-PCR
Information
Methods
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
  Background
  Results
  Conclusion

## Slide 18: Conclusion
q-PCR
  Highly sensitive and reproducible
  Reduces the number of colonies for further analysis (via Southern Analysis)
  Superior to Regular PCR
    Not limited by false negatives
    False positives by primer-primer interaction was not an issue
    Detects multiple inserts of the gene because of its real time quantitative approach

## Slide 19: Conclusion
q-PCR vs. FISH
  q-PCR is superior in the detection of BAC-based constructs
  FISH is prone to false positives and false negatives
    q-PCR was able to identify both the false positives and false negatives

## Slide 20
Advantages of q-PCR as a method of screening for gene targeting in mammalian cells using conventional and whole BAC-based constructs
Julio Go´mez-Rodrı´guez, Valance Washington, Jun Cheng, Amalia Dutra, Evgenia Pak, Pentao Liu, Daniel W. McVicar and Pamela L. Schwartzberg
Received March 31, 2008; Revised July 28, 2008; Accepted July 31, 2008; Published online 18 August 2008
Nucleic Acids Research, 2008, Vol. 36, No. 18 e117
q-PCR